## Slide 1: Cellular Communications for Utilities
Presented by John Kretzschmar & Jon Scott

## Slide 2: Cellular Technology
    A communication network where the last link is wireless.
    The network is distributed over areas call ‘cells’ that are served by at least one transceiver.
    When joined together, these cells provide radio coverage over a wide area.
    This cellular coverage enables numerous portable devices such as phones, tablets and laptop computers to operate anywhere within the network.

## Slide 3: LTE Variations
LTE CAT 3
100 Mbps
LTE-MTC CAT NBI
50 Kbps
LTE CAT 4
150 Mbps
LTE CAT 6
300 Mbps
Etc…
LTE-MTC CAT 1
10 Mbps
LTE-MTC CAT 0
1 Mbps
LTE-MTC CAT M1
256 Kbps
Lower Power/Cost, IoT Applications
Faster Download Speeds, Low Latency

## Slide 4: Cellular Technology
    LTE is still the cellular technology of choice around the world
    Serving over 6.6 devices as of January of this year.
    LTE offers high bandwidth connectivity with predictable latency
    It is extremely secure, has a large ecosystem of suppliers and offers a robust roadmap

## Slide 5: How fast is 4G LTE?
In theory, LTE's maximum speed is 100Mbps. In practice, it tops at 15Mbps. Of course, it all depends on where you're located.
What about LTE-A and LTE+?

## Slide 6: LTE-A, LTE-Advanced, 4G+, and LTE+
LTE-A, LTE-Advanced, 4G+, and LTE+ are all acronyms for the same 4G service. It's a faster version of LTE.
How fast is LTE-A? In theory, LTE-A data rates are up to 300Mbps. In practice, you can expect between 40 to 90Mbps.

## Slide 7: The Future of LTE
The future of 4G LTE is still bright. Some capabilities of the 5G are not available yet and will not be needed right away for existing applications that are functioning well with the bandwidth and latency offered by 4G LTE networks. 4G devices will continue to work and can often wait to upgrade to 5G. Because 4G LTE and 5G share spectrum, and 5G devices offer failover to 4G for areas where 5G is not yet established, the migration from LTE to 5G will occur over a period of at least a decade or more.

## Slide 9
Evolution to 5G Technology

## Slide 10: 5G Technology
    5G brings more improvements, but it’s comprised of a suite of new technologies
      Small cells
      Millimeter waves
      Massive Multiple-input Multiple-output (MIMO)
      Beamforming
      Full duplex

## Slide 11: Small Cells
    Small cells are miniature cell phone towers that can be placed in inconspicuous places like light poles and the roofs of buildings
    They don’t require as much power as full-sized towers, and perform better when clustered together

## Slide 12: Millimeter Waves
    Small cells transmit data using millimeter waves, which get their name from their narrower-than average wavelength
    They occupy frequencies in the 30-300GHz range — high enough to avoid interference from surrounding signals, but too high to pass through physical barriers
    In some cases, the leaves of trees are enough to interrupt a download

## Slide 13: Multiple Input Multiple Output (MIMO)
    Millimeter waves have limitations, but they’re a good fit for MIMO — a wireless system that uses multiple radios to send and receive data simultaneously
    The 4G LTE networks of today support a maximum of eight transmitters and four receivers, but 5G cell towers can theoretically support dozens

## Slide 14: Beamforming
    More radios mean more interference; that’s where beamforming comes in
    At its most basic, beamforming uses algorithms to choreograph wireless signals’ movements and increase their strength by focusing them in a beam

## Slide 15: Full Duplex
    Full duplex helps boost the signal even further
    Most current-gen cell towers and devices cannot transmit and receive at the same time, but full duplex phones can route incoming and outgoing signals simultaneously, potentially doubling bandwidth

## Slide 16
5G Limitations
    5G won’t provide nearly as much coverage as 4G LTE, or even 3G. In many ways and it will seem more like Wi-Fi than a cellular technology
    5G transmitters will be set a closer to the ground. This requires a lot of ground coverage hardware to insure you’ll have a reliable signal

## Slide 17
5G Limitations
    The high frequencies and correspondingly low wavelengths of 5G will have difficulty penetrating solid objects such as walls, windows, and even trees
    For these and other reasons, industry experts expect 4G LTE to advance alongside 5G
    Collaboration is already underway on gigabit 4G LTE connectivity, and at least one carrier has said portions of its existing network reach gigabit speeds.

## Slide 18: Cellular Technology Roles
    Residential load control
    3rd party access
    Industrial load control
    Interruptible programs
    Video feed from security cameras
    Back hauling AMI data
    Remote disconnect/ reconnect
    Remote meter reads
    Full AMI systems
18

## Slide 19: Advantages of Public Cellular AMI and Targeted Cellular Solutions

## Slide 20
    Remote reads
    Remote connect / disconnect
    Outage management (With alerts)
    Voltage management (With alerts)
    Time-Of-Use and off-cycle reads
    Two-way communications networks
    Many AMI “flavors”
AMI | ADVANCED METERING
Key Features

## Slide 21
    Reconnects and transfers of service handled remotely and immediately
    Greater reading and billing accuracy
    Collect meter reads on demand
    Directly address customer complaints
    Re-reads for discontinued, move-ins, move-outs
    Allows time-based rate programs and pricing, e.g. time of Use, peak rebates
AMI | ADVANCED METERING
Known Benefits
Saves utility money and improves service quality

## Slide 22
    Improved system
    Voltage monitoring can lead to better regulation, improved capacitor and regulator placement and more accurate voltage-drop analysis
    Improved load information
    Leads to better load studies and analysis, resulting in improved planning and system design
    Improved reliability monitoring
    Can lead to improved outage response, proper system-protection analysis, decrease in outages and outage time, raising reliability indices
    Improved monitoring and information flow
    Better management of critical assets such as transformers and capacitors
    Pinpoint and reduce system losses
AMI | ADVANCED METERING
Benefits for Operations

## Slide 23
AMI | ADVANCED METERING
Cost Considerations
    Large orders to offset their costs
    Proprietary collection networks
    Utility IT resources
    High infrastructure costs
    High software costs
    Frequency licensing fees
    Maintenance of communications system
Despite the benefits, AMI systems have been cost prohibitive for many utilities.

## Slide 24
AMI | ADVANCED METERING
Cost Considerations
However, technological advances have come together that make AMI more affordable for all utilities.
    Hosted software
    Public cellular communications
    Self-healing (mesh-cellular hybrid)
    Less reliance on costly utility infrastructure
AMI Cloud Database

## Slide 25
AMI | ADVANCED METERING
Advantages of Public Cellular Communications
    Incrementally deploy your meters
    Freedom of meter placement
    Essential service / quick repair
    No frequency rental fees
    Zero utility infrastructure
    No maintenance costs
    Security

## Slide 26
AMI | ADVANCED METERING
Advantages of a Hosted System
    Secure data storage (whitepapers available)
    Does not require IT resources
    Accessible from any device
    Fully scalable to any need
    Always up to date

## Slide 27
CONCLUSION
Public Cellular Communications & Technological Advances Have Simplified AMI
    Freedom to deploy on your schedule
    Does not require IT resources
    Zero upfront network and infrastructure costs
    Lower operational costs
    Contact us today to learn more

## Slide 28: Thank You
Jon Scott (404) 451-8444
jonathan.scott@nighthawkcontrol.com
John Kretzschmar
(864) 590-2883
john@samscometering.com