## Slide 1: The Theory of AC and DC Meter Testing
Prepared by Tom Lawton, TESCO
For North Carolina Electric Meter School
Polyphase
Thursday, June 16, 2022 10:15 AM

## Slide 2: A Little History
1800 Volta
  First electric battery
1830-31 Faraday and Henry
  Changing magnetic field can induce an electric current. Build first very crude electric motors in lab.
1832 Pixii
  First crude generation of an AC current.
1856 Siemens
  First really practical electric motor
1860s Varley, Siemens and Wheatstone
  Each develop electric dynamos (DC Generators).
Notes: Werner von Siemens was a German engineer who developed the modern dynamo and held one of the first US patents on electrical meter. Charles Steinmetz research into hysteresis led to better AC motors and transformers.

## Slide 3: A Little History
1870s
  First electric railroad and street lights in Berlin (DC).
1880
  First electric elevator (DC).
1885-88 Thomson, Ferraris, Tesla
  Each develop AC electric induction motors.
  Tesla is granted a US patent for induction motor in 1888.
1890 Dolivo-Dobrovolsky
  First three phase generator, motor and transformer
Notes: Werner von Siemens was a German engineer who developed the modern dynamo and held one of the first US patents on electrical meter. Charles Steinmetz research into hysteresis led to better AC motors and transformers.

## Slide 4: A Little History
Edison and Westinghouse
  Edison favored DC power distribution, Westinghouse championed AC distribution.
  The first US commercial electric systems were Edison’s DC systems.
First AC system was in 1893 in Redlands, CA. Developed by Almirian Decker it used 10,000 volt, three phase primary distribution.
Siemens, Gauland and Steinmetz were other pioneers.
Notes: Werner von Siemens was a German engineer who developed the modern dynamo and held one of the first US patents on electrical meter. Charles Steinmetz research into hysteresis led to better AC motors and transformers.

## Slide 5: War of the Currents
Thomas Edison
George Westinghouse
Nikola Tesla

## Slide 6: Westinghouse
1884 – George Westinghouse establishes the Union Switch & Signal Co. in Pittsburgh, PA
Buys the U.S. rights to a transformer patented in Europe
The company reorganizes as the Westinghouse Electric and Manufacturing Company
William Stanley joins the company as the chief electrical engineer and Oliver B. Shallenberger resigns as an officer in the U.S. Navy to work under him as the chief electrician.
George Westinghouse

## Slide 7: AC Starts to Win
Stanley and Schallenberger: They refine the transformer design and in 1886 Stanley demonstrates the first complete system of high voltage AC transmissions including generators, transformers, and high voltage transmission lines.
AC had none of the issues of DC (voltage drop in long lines and a lack of an easy way to increase or decrease the voltage). However there was no meter that could accurately record the usage of electricity on AC circuits.
William Stanley, Jr.
Oliver Schallenberger

## Slide 8: Thomas Edison - 1889
"Fooling around with alternating current is just a waste of time. Nobody will use it, ever."
- Thomas Edison, 1889

## Slide 9: 1888: A Young Serb Named Никола Тесла (Nicola Tesla) Meets George Westinghouse
Nicola Tesla, "The Wizard of The West"
1893: World’s Fair Chicago lighted by Westinghouse / Tesla
1882: Induction Motor
1888: Westinghouse, American entrepreneur and engineer meets Tesla

## Slide 10: 1893: Westinghouse Awarded the Contract for Powerhouse at Niagara Falls
Edward Dean Adams power station at Niagara, with ten 5,000-horsepower Tesla/Westinghouse AC generators — the culmination of Tesla's dream. (Courtesy Smithsonian Institution)

## Slide 11: AC Theory - History
By 1900 AC power systems had won the battle for power distribution.
  Transformers allowed more efficient distribution of power over large areas.
  AC motors were cheaper and easier to build.
  AC electric generators were easier to build.

## Slide 12: AC vs DC
Direct Current (DC) – an electric current that flows in one direction.(IEEE100)
Alternating Current (AC) – an electric current that reverses direction at regularly recurring intervals of time. (IEEE100)

## Slide 13: AC Circuits
An AC circuit has three general characteristics
  Value
  Frequency
  Phase
In the US, the household value is 120 Volts with other common voltages being 208, 240, 277 and 480 Volts. The frequency is 60 Hertz (cycles per second).

## Slide 14: AC Theory – Sine Wave

## Slide 15: AC Theory - Phase
Here current LAGS voltage.

## Slide 16: AC vs DC
In DC theory we learned
  Ohm’s Law
    Voltage = Current x Resistance
    V = IR
  Power
    P = I2R = V2/R
For AC we would like the same equations to apply.
  Specifically we want to be able to say that a DC voltage of 10 Volts applied to a resistor of value R produces the same power dissipation as an AC voltage of 10 volts applied to the same resistor.

## Slide 17: AC Theory – RMS
For DC voltage to equal AC voltage we need

## Slide 18: AC Theory - RMS
RMS Value

## Slide 19: AC Theory – RMS
So if we want to have the V in our equation for an AC signal represent the same value as the its DC counterpart we have
By convention in AC theory we refer to VDC as the RMS (Root Mean Squared) voltage.
When we talk about AC values we always mean the RMS value not the peak value unless we say so specifically

## Slide 20: AC vs DC
V = IR
P = VI = I2R = V2/R

## Slide 21: AC Theory – Resistive Load
Resistors are measured in Ohms. When an AC voltage is applied to a resistor, the current is in degrees. A resistive load is considered a “linear” load because when the voltage is sinusoidal the current is sinusoidal.

## Slide 22: AC Theory – Inductive Load
Inductors are measured in Henrys. When an AC voltage is applied to an inductor, the current is 90 degrees out of phase. We say the current “lags” the voltage. A inductive load is considered a “linear” load because when the voltage is sinusoidal the current is sinusoidal.

## Slide 23: AC Theory – Capacitive Load
Capacitors are measured in Farads. When an AC voltage is applied to a capacitor, the current is 90 degrees out of phase. We say the current “leads” the voltage. A capacitive load is considered a “linear” load because when the voltage is sinusoidal the current is sinusoidal.

## Slide 24: AC Theory – Active Power
Active Power is defined as P = VI
Power is a rate, i.e. Energy per unit time.
The Watt is the unit for Power
  1 Watt = 1000 Joules/sec
Since the voltage and current at every point in time for an AC signal is different, we have to distinguish between instantaneous power and average power.
Generally when we say “power” we mean average power.

## Slide 25: AC Theory – Energy
Energy is power integrated over a period of time.
The units of Energy are:
  Watt-Hour (abbreviated Wh)
  Kilowatt-Hour (abbreviated kWh)
A Wh is the total energy consumed when a load draws one Watt for one hour.

## Slide 26: AC Theory – Instantaneous Power
For a resistive load:
P = 11520 Watts

## Slide 27: AC Theory – Instantaneous Power
For an inductive load:
P = 0 Watts

## Slide 28: AC Theory – Instantaneous Power
For an capacitive load:
P = 0 Watts

## Slide 29: AC Theory – Complex Circuits
Impedance – The equivalent to the concept of resistance for an AC circuit. It is also measured in Ohms. Designated by the symbol X.
In AC circuits non-resistive impedance affects both the amplitude and phase of the current.
A resistor R has an impedance which is frequency independent. There is no phase shift.
An inductor has an impedance which is proportional the frequency, XL = 2πfL. The phase is shifted by 90 degrees lagging.
A capacitor has an impedance which is inversely proportional the frequency, XC = 1/2πfC. The phase is shifted by 90 degrees leading.

## Slide 30: AC Theory – Complex Circuits
Amplitude (Current)
Phase (Current)
VC
V
VL
VC
VR

## Slide 31: AC Theory – Instantaneous Power

## Slide 32: Time Out for Trig (Right Triangles)
The Right Triangle:
The Pythagorean theory
c2 = a2 + b2

## Slide 33: AC Theory – Power Triangle (Sinusoidal Waveforms)
If V = sin(ωt) and I = sin(ωt - θ) (and the load is linear)
then
Active Power = VIcos(θ) Watts
Reactive Power = VIsin(θ) VARs
Apparent Power = VI VA
Power Factor = Active/Apparent = cos(θ)
Watts
VARs
VA

## Slide 34: Harmonics Curse of the Modern World
Every thing discussed so far was based on “Linear” loads.
  For linear loads the current is always a simple sine wave. Everything we have discussed is true.
For nearly a century after AC power was in use ALL loads were linear.
Today, many loads are NON-LINEAR.

## Slide 35: Harmonic Load Waveforms
ANSI C12.20 now addresses harmonic waveforms as well as sinusoidal.
Chart: 
Chart: 
Chart: 
Chart: 
Test waveforms being proposed for ANSI C12.20.
Chart: 
Chart: Voltage

## Slide 36: AC Theory - Phasors
An easier way to view AC data

## Slide 37: AC Theory - Phasors
The length of the phasor is proportional to the value of the quantity
The angle of the phasor (by convention phase A is drawn as horizontal) shows the phase of the quantity relative to phase A voltage.
Here the current “lags” the voltage by 30 degrees.

## Slide 38: AC Theory - Phasors
Phasors are particularly useful in poly-phase situations

## Slide 39: New Energy Definitions
At the moment there is no non-sinusoidal definition for VA
New ANSI Standard coming soon
C12.31

## Slide 40: New Definitions
RMS Voltage
Basic Definition
Time Domain
Frequency Domain
Waveform

## Slide 41: New Definitions
RMS Current
Basic Definition
Time Domain
Frequency Domain
Waveform

## Slide 42: New Definitions
Active Power
Basic Definition
Time Domain
Frequency Domain

## Slide 43: New Definitions
Apparent Power
Basic Definition
Time Domain
Frequency Domain

## Slide 44: What about DC?
We have had DC Metering since the 1870’s.
The first patented meter was a DC meter in 1872, six years before the first AC meter.

## Slide 45: Elihu Thomson
1889 Thomson introduced his recording wattmeter (AC or DC – a commutator-type meter).
This was the first true watthour meter, and it was an immediate commercial success, many utilities adopting it as their "standard" model.
Although this meter was initially designed for use on AC circuits, it worked equally well with the DC circuits in use at the time.
The introduction and rapid acceptance of induction-type watthour meters in the late 1890s relegated the use of this commutator-type meter to DC circuits.

## Slide 46: DC Theory?
No need for new definitions. Power is simply VA. If we can measure the fundamental Volt and the fundamental Amp then we can create a Standard to measure against and can effectively test our DC meter.

## Slide 47: What about DC?
There are still a number of DC meters out on our systems, primarily in the larger, older urban areas such as San Francisco and New York City.
There has been no effective way to test these legacy meters for some time. This is shortcoming was highlighted as new DC metering applications have begun to make an appearance on the grid and are demanding we find a solution (e.g. DC superchargers)
Using labs with traceable Voltage sources and measurement capabilities and traceable Current sources and measurement capabilities we are now starting to do this.

## Slide 48: ANSI C12.32
As always, the theory is only the start. We now need to take this theory and create a practical process. For AC Meters we have been using ANSI C12.1 for many years to guide us on how to move from theory to practice.
We have never had a comparable Standard for DC Metering
ANSI Standard ANSI C12.32 for Electricity Meters for the Measurement of DC Energy has been developed over the past several years and is actively being balloted and is expected to be released in 2022.
This Standard lays out the tests, the definitions, the acceptable performance levels for accuracy as well as functional testing.
Definitions are given and the practical means of type testing as well as acceptance testing are given.

## Slide 49: Questions and Discussion
Tom Lawton
President
tom.lawton@tescometering.com
TESCO – The Eastern Specialty Company
Bristol, PA
215-228-0500
This presentation can also be found under Meter Conferences and Schools on the TESCO website: tescometering.com
ISO 9001:2015 Certified Quality Company
ISO 17025:2017 Accredited Laboratory