## Slide 1
Instructor: Dan Hollow - Rocky Mountain Regional Sales Manager - TESCO, The Eastern Specialty Company
TESCO is a wholly owned subsidiary of Advent Design Corporation of Bristol, PA. Dan has worked for TESCO since 2015, originally hired to sell the Meter Manager Meter Asset Management Software and then was given the Rocky Mountain Region Sales Territory in late 2016 and now sells the TESCO products in 4 states (CO, WY, UT, AZ, and the western half of KS, NE, SD, and ND). Dan has been working in the utility industry since 1988 and began his career in the utility industry as the Test Department Supervisor for Aptech and accepted an outside sales position for Aptech in 1992 and has been in outside sales ever since. Dan has worked for companies such as UTS/Itron, Datamatic, Metrum Technologies/Aclara, and TESCO.
Dan has worked in the technology industry since 1980 and has worked in other industries such as Banking Equipment, Industrial CNC Controls, Process Control and Flight Simulator Equipment prior to working in the utility industry.
2017 Meter School
Test Switch Operation & Accessories

## Slide 2
Purpose:
To acquaint the attendees with the use and purpose of Meter Test Switches
Course Breakdown of Topics:
Using Test Switches
Meter Test Switch Specifications
Meter Test Switch Configurations
Meter Test Switch Accessories
Pre-Wired Transformer Rated Enclosures
2017 Meter School

## Slide 3
2017 Meter School
Typically found in residential metering
Meters are capable of handling the direct incoming amperage
Meter is connected directly to the load being measured
Meter is part of the circuit
When the meter is removed from the socket, power to the customer is interrupted
Typical Self Contained Service

## Slide 4
2017 Meter School
Meter measures scaled down representation of the load.
Scaling is accomplished by the use of external current transformers (CTs) and sometimes voltage transformers or PTs).
The meter is NOT part of the circuit
When the meter is removed from the socket, power to the customer is not effected.
Transformer Rated Service

## Slide 5
2018 Meter School
Transformer Rated Service
5A
PHASE A
SOURCE
PHASE C
PHASE B
LOAD
400A
400A
400A
5A
5A
5A
5A
5A
9S Meter Installation with 400:5 CT’s

## Slide 6
2017 Meter School
Testing current transformers while they are in service can be a dangerous operation if certain safety procedures are not followed. The secondary loop of a current transformer must NEVER BE OPENED when service current is present in the primary. When there is current in the primary, and the secondary of a current transformer is open circuited, the voltage across the secondary can rise to hundreds and even thousands of volts, creating an extremely dangerous situation. The open CT secondary voltage magnitude varies with CT design and primary
current flow. The high voltage that is present on the open secondary of an energized current transformer generates two great hazards. The first hazard is ELECTRICAL SHOCK TO TESTING PERSONNEL. The second hazard is THE BREAKDOWN OF THE CURRENT TRANSFORMER INSULATION. Both hazards can be avoided provided that the secondary of the current transformer is never opened. The safest current transformer installations for testing are those that have a Test Switch as part of the secondary loop. A Test Switch is a device that will facilitate inserting instrumentation in the current transformer secondary loop without the danger of opening the circuit.
SAFETY

## Slide 7
2017 Meter School
Typical Connections for Common Meter Forms

## Slide 8
2017 Meter School
Test Switch Specifications
ANSI C12 Definitions
Test Switch Materials
Plating
Barriers
Wiring Connections
What to look for
Covers

## Slide 9: ANSI C12.9 Test Switch Definitions

## Slide 10
ANSI C12.9
Test Switches

## Slide 11
ANSI C12.9 General Test Switch Specifications

## Slide 12
Test Switch Configurations
Layout
Handle Colors
Reversed vs. Normal Potentials
Current Links
Base Sizing
Barrier Locations

## Slide 13
Test Switch Accessories
Test Plugs
Safety Covers
Test Switch Isolators
On installations that contain Test Switches, test leads terminated with a test switch
safety test probe (test plug) should be used for CT testing. This provides a “make-before-break” connection to prevent accidental opening of the current transformer secondary loop.

## Slide 14
ANSI C12.9 Test Jack Specifications

## Slide 15
ANSI C12.9 Test Plug Specifications

## Slide 16
Pre-Wired Transformer Rated Enclosures
Cover Types
Wiring
Sockets

## Slide 17
2017 Meter School
Questions?

## Slide 18
2017 Meter School
3 Quiz Questions Multiple Choice
1. Which type of metering service typically has a test switch?
Self Contained
Transformer Rated
Gas
2. Why would you want to reverse the potentials on test switch?
Aesthetics
To use multiple voltages
To de-energize the potential blades when open for safety
3. What is the purpose of a current link on a test switch?
To enable connection of the test jack and shunt in the current pair to complete the current loop.
To connect the current pairs to the potentials
To eliminate the need for barriers between the poles